## Slide 1: One Hands-On Tech club Two Groups
3D Printing
Small Computers

## Slide 2: Welcome to H.O.T. www.handsontech.org
Our Purpose:
Forum for interaction
  Many hobbyists build/tinker in isolation
  Make new friends with common tech interests
Learn together
  Lots of fun new tech to explore
  Share expertise, help each other
Build something
  Hands-On learning
  Make something fun & useful

## Slide 3: New to the club? Welcome!
Wondering what H.O.T. is all about?
This is a hands-on group, so we may be in the middle of a series of meetings on our way to building something interesting
Go to handsontech.org>New Members for a specially designed launching point for new members!
Please take the time to look through a few presentations at handsontech.org>Small Computers or handsontech.org>3D Printing.
  Presentations are always available online after our meetings for reference and as self-paced projects

## Slide 4: Club communications are via Email & Web !
To join our email list(s), fill membership form at handsontech.org>New Members
  When asked for your email address, use a gmail email address if possible (we use google forums & they are picky)
  You will be added automatically to our Hands-On Tech (H.O.T.) overall email list
  You will also be added to the Small Computers and/or 3D Printing mailing lists and forums if you expressed interest in the membership form.
Meeting calendar is at handsontech.org

## Slide 5: Home Monitoring using Cellular IoT*
Hands-on Technology – Small Computers
  February 22, 2022
  Bob Jessup
  _______________________________________
  * Internet of Things

## Slide 6: The Problem – Remote Monitoring
Snowbird Concerns
  Failed furnace or A/C, flooding, doors, lights
Possible Solutions
  Honeywell Winter Watchman $0 / month
  Wifi router, cameras, thermometers, etc. $80 / month
  Security monitored services $50 / month + $80 / month
  Human homewatch service $50 - $100/ month
  IoT cellular sensors < $2 /month for 1 MByte

## Slide 7: Cellular Solutions – Get on the Google
Hologram offers one free pilot SIM up to 1MB / month
3G Sim 800 modems w/ on board processor (obsolescent)
LillyGo ($50) includes SIM7000G & ESP32 processor
Global ($30) 1.5-inch SIM7000A (iffy sim card holder)
Botletics ($65) Arduino shield with SIM7000A modem

## Slide 8: Selected Approach: Botletics & ESP32
Botletics Sim7000A Arduino shield (available tomorrow)
Hologram SIM card
Sensors to monitor 3 floors
Apply ESP32 to communicate wirelessly with sensors
____________________________________________
..besides, somebody needed a pandemic project..

## Slide 9: Where We are Going:
HUB
IFTTT
Hologram
(Cellular)
Dweet
Google Mail
Google Sheets
Cellphone Widget
Home Assistant
Sensors
Snow
Sun
WIFI ROUTER
Notes: Black path is primary path

## Slide 10: Primary Path: Remote Sensor to Cellphone
HUB
IFTTT .COM
Hologram
(Cellular)
Google Mail
Cellphone Widget
Sensors
WIFI ROUTER
Notes: Black path is primary path

## Slide 11: Sensors - Hub Configuration
Sensors are wireless access point (AP) servers to pass info to HUB w/o a router.
1st Floor HUB (Client)
Kitchen (AP)
Upstairs Bedroom (AP)
Basement (AP)
Temp
Doors
Light
Flood
Ambient_1 192.168.4.1
Ambient_2 192.168.4.2
Ambient_3 192.168.4.3
Hum
55.3
/temperature
192.168.4.1

## Slide 12: Sensor Wiring ESP32, BME280, SSD1306
Why ESP32?
Powerful $9 processor
(less $ if from China)
Wireless antenna
Strong wifi Library
Arduino based
Easy to program
Strong on-board
3.3v .8A regulator

## Slide 13: HUB Wiring: Sensor + Cellular Modem

## Slide 14: Theory of Operation
Sensors are set up as wireless access point AP servers
* They return data upon receiving http GET requests
HUB is base unit (gateway) with cellular modem and processor
* It can function alone or collect sensor data using http
HUB transmits data hourly in JSON format
Messages require 1.333 kB for data and overhead.
    * 1.333 kB x 24 hrs x 31 days = 992kB / month

## Slide 15: JSON: Human Readable Data
JSON – JavaScript Object Notation
Simple format is {label:data,label:data}
  Example: {“temperature”:”57”,”humidity”:”62”}
IFTTT allows only 3 values, but we need more
  Workaround: send all our values as one:
  {“Value1”:”57,57,56,58,-62,62,64,62,57”}

## Slide 16: Hologram Provides Cellular Path to Cloud
HUB
IFTTT
Hologram
(Cellular)
Google Mail
Cellphone Widget
Sensors
Notes: Black path is primary path

## Slide 17: Hologram: Cellular Connectivity to the Cloud
Hologram enables connection and management of devices worldwide
  Claim 470+ global cellular networks
Hologram offers free pilot ioT SIM card which includes 1MB/mo
  Additional cards cost $1.50/month plus $.40 per MB
  Each card includes mini (2FF), micro (3FF), Nano (4FF) size

## Slide 18: IFTTT Links (Disparate) Services
HUB
IFTTT
Hologram
(Cellular)
Google Mail
Cellphone Widget
Sensors
Notes: Black path is primary path

## Slide 19: IFTTT – IF THIS Then THAT
IFTTT Links Services
IFTTT webhook event (HB) emails data and adds to Google Sheets. (IF HB THEN email data and add to Google Sheets)
IFTTT is also set up to pass weather info every 3 hours.
Use a dedicated gmail account to set up your IFTTT account.

## Slide 20: Data Appears on Phone Home Screen
HUB
IFTTT
Hologram
(Cellular)
Google Mail
Cellphone Widget
Sensors
Notes: Black path is primary path

## Slide 21: Reports Appear on Phone Home Screen
The IFTTT webhook (HB) forwards data to the subject line
Set up a 2”x2” gmail widget on the home screen of your phone
  Shows 2 hrs sensor data, latest weather rpt
Time, Event, 5 temps, 2 doors, 5 lights, 2 moisture, 1 SS, 4 humidity:
14:47 HB 54,55,56,58,50,0,0,00,05,03,93,00,00,-62,25,29,30,32
12:47 HB 53,54,56,56,50,0,0,00,05,03,96,00,00,-60,24,28,32,31
12:02 temp 28 AM Clouds/PM Sun today! High 32, Low 22.

## Slide 22: Secondary Path – Google Sheets
HUB
IFTTT
Hologram
(Cellular)
Google Mail
Google Sheets
Cellphone Widget
Home Assistant
Sensors
Notes: Black path is primary path

## Slide 23: Secondary Path – Google Sheets
IFTTT populates the spreadsheet for system performance
DateTime, Event (HB, Weather) data are appended
IFTTT also updates the 2nd row with HB events
Home Assistant can open a card to monitor this row
Eliminates the need to track the latest inserted row

## Slide 24: IF IFTTT Fails Then Dweet!!
HUB
IFTTT
Hologram
(Cellular)
Dweet
Google Mail
Google Sheets
Cellphone Widget
Home Assistant
Sensors
Notes: Black path is primary path

## Slide 25: Dweet.io Provides a Free Service
Displays the last 5 messages within past 24 hours
Use to view information if (when) IFTTT path fails
No credentials, passwords, etc.; simply make up an identifier
I use the 15 digit SIMCOM modem imei as my identifier
Retrieve at dweet.io/get/dweets/for/(your identifier)

## Slide 26: Cellular IoT Home Monitor
HUB
IFTTT
Hologram
(Cellular)
Dweet
Google Mail
Google Sheets
Cellphone Widget
Home Assistant
Sensors
SNOW
SUN
WIFI ROUTER
Notes: Black path is primary path

## Slide 27: Troubleshooting Tips - Remote
Hologram, IFTTT dashboards
Dweet provides alternate report if failure occurs downstream
External timer to reboot system periodically
Run duplicate system using same software
Neighbors can read sensors directly on cellphone
Catastrophic failure – exchange units

## Slide 28: To Do List – Florida
Verify Florida vendors via cellular IoT
  Lawncare, bush trimming, weed & pest control
  Manage sprinklers remotely
  Camera to send still photos

## Slide 30
Hardware – A collection of all the parts you can physically Touch

## Slide 31: Hub Progression – Oct 2021 Maine

## Slide 32: Hub Parts List
Description | Amazon | AliExpress | Notes
MELife 2 Pack for ESP32 ESP-32S Development Board (not Mini!) | $16.99/pair | $1-$3 | Onboard AMD1117 regulator adequate for modem
Botletics SIM7000A LTE CAT-M1 NB-IoT Cellular + GPS + Antenna | $65 |  | 
Ultronics .96 Inch OLED Module 128x64 SSD 1306 .96” Display | $3 - $10 |  | I2C bus; optional, but convenient during development/debug
BME280 temp/hum sensor | $15 was $5 | $1.80 | I2C bus;
ELEGOO 3pcs Breadboard 830 Point Solderless Prototype | $9.99/3 |  | OR: Prototype PCB for Arduino R3 Shield Board DIY $8.90/4
Breadboard jumper wires | $10/kit |  | Precut sizes, convenient
BN-LINK 7 Day Heavy Duty Digital Programmable Timer | $13.99 |  | Battery backup timer

## Slide 33: Hub Parts List 2 – PCB & Enclosure Options
Description | Amazon | Notes
ElectroCookie Solderable Breadboard PCB Double Column | $12.99/3 | PCB having same hole pattern and connections as breadboard!
AwClub Waterproof Dustproof ABS Plastic Junction Box Model 115*90*55 | $6.99 | Use with prototype Arduino shield; transparent cover to view OLED display
OR: |  | 
Prototype for Arduino UNO R3 Shield DIY | $8.90/4 | Hole pattern matches Botletics/Arduino
AwClub Waterproof Dustproof ABS Plastic Junction Box Model 100*68*10 | $6.99 | Use with prototype arduino shield; transparent cover to view OLED display
40 pin female header sockets |  | Allows plugging in your compnents instead of soldering
40 pin male breakaway header |  | Plug proto board onto Botletics

## Slide 34: Maine Basement Sensor
(High water mark)

## Slide 35: Maine Kitchen Sensor in Rpi case (light, front door, temp)

## Slide 36: Florida Sensor

## Slide 37: Florida Sensor Parts List
Description | Amazon Price | AliExpress + Shipping | Notes
MELife 2 Pack for ESP32 ESP-32S Development Board | 16.99/pair | Less $ | Option: Wemos D1 Mini 8266 (1 only) $3 - $8
Ultronics .96 Inch OLED Module 128x64 SSD 1306 .96” Display | $3 - $10 | Less $ | I2C bus; optional, convenient
BME280 temp/hum sensor | $15 | $1.80 | I2C bus
ELEGOO Breadboard 415 Point Solderless Prototype |  |  | 
Option: ATPWONZ Plastic Boxes | $14.99/10 |  | Enclosure encompasses breadboard. Drill ventilation holes.

## Slide 38: Software – Instructions that tell a computer what to do

## Slide 39: Software & Services
Description | Base Cost | Source | Why is Necessary
Hologram.io Service | $0 | Google it | Cellular access, ioT SIM card
IFTTT.com Service | $0 for up to 5 applets | Google it | Pass data to gmail, populate google sheets
Dweet.io Service | $0 | Google it | IFTTT backup
Arduino IDE Software | $0 | Google it | Edit & Load ESPxx sketch
AmbientHUB Software | $0 | H.O.T 2/22/2022 | Hub Software
AmbientAP Software | $0 | H.O.T 2/22/2022 | Optional Sensor Software
Arduino Libraries (listed as #include in Ambient software) | $0 | Import using IDE | Building blocks for Ambient software
Google Drive, Sheets, Gmail | $0 | Google | Dedicated email, analysis

## Slide 40: Options – Alert Mode or Snooze Mode
Alert Mode responds immediately
  HUB stays awake, polling sensors
  Sensors can stay awake or sleep until interrupt event
  HUB uploads hourly heartbeat data as well
  Requires temperature sensors outside case

## Slide 41: Options – Alert Mode or Snooze Mode
Snooze Mode simply sends data Hourly
  HUB sleeps 48 minutes, wakes 12 minutes
  Sensors sleep 8 minutes, wake 2 minutes
  HUB can read all 3 sensors while awake
  Enables internal temperature sensors to stay cool

## Slide 42: Ambient_AP Sensor Software
Compile-time options are explained in the top section
Setup()
  reads sensors & starts AP to respond to http requests
Loop() execution
  If snooze mode, do nothing until its time to go to sleep
  Else
    Read sensors at timed intervals
  Repeat Loop()

## Slide 43: Ambient_HUB Software
Compile-time options are explained in the top section
Setup()
  initialize hardware
Loop() execution
  Reads sensors when & sends an event to IFTTT immediately if alarmMode = 1
  Heartbeat data is sent to IFTTT or Dweet.io each hour
  If Snooze Mode, Sleeps 48 minutes after which time setup is run again before repeating Loop() for 12 minutes

## Slide 44: Troubleshooting Tips - Local
Interpret OLED displays and LED blink rates
Embedded Print Statements to status monitor in test mode
EN button on ESP’s reboot system tests entire loop on startup
Misc software flags can be adjusted to diagnose issues

## Slide 45: To Do List - Software
AT commands to eliminate the fona library, reduce 1.3k / msg
Evaluate the 1.5-in Global.com unit to reduce the size and cost
  Ordered one Jan 9, 2022; it arrived Jan 24 from AliExpress
MQTT using online broker?
Evaluate ESP Now for sensor-hub communication

## Slide 46: The Devil is in the Details
Where’s the beef?!
Moving on . .

## Slide 47: What Exactly IS this Project?
Sensors monitor ambient conditions in empty home x 2
Sensors are hard wired – no batteries
It is NOT a security system
It is NOT FCC approved for resale (FCC 47 cfr 2.803)

## Slide 48: Alphabet Soup – Cellular Terms
Cellphones sell access by the GigaByte ($2/GB)
3G GSM – Global System for Mobiles (AT&T, T-Mobile)
3G CDMA – Code Division Multiple Access (Verizon, Sprint)
4G HSPA – High Speed Packet Access = faster version of 3G GSM
“4G” LTE – Long Term Evolution – Verizon, fast data performance technology designed with an eye on 5G; 4G LTE speed = 3G x 10
5G – 4G LTE x 100 (download a 2-hr movie in < 10 seconds)

## Slide 49: Alphabet Soup – Cellular Terms
ioT sells access by the Mbyte (1$/MB) x 1000 = $1000/GB
  NB-IoT – 200 kHz BW 30/60 DnLd/UpLd kbps, 35km range
  LTE-M – 1.4 MHz BW 300/375 DnLd/UpLd, 15-20 km range
Simcom LTE-M/NB-IoT Modems – SIM7000A,C,E,G
  America, China, Europe, Global

## Slide 50: Sensor Wiring (ESP32)
All labels are as printed on ckt board, not schematic pins!
Function is in ()
External power is supplied to the ESP32 via USB cable
ESP32 3.3 volt pin supplies power to all components
D22(SCL)
D21(SDA)
GND
3.3v
SCL
SDA
GND
Vcc
SCL
SDA
GND
Vcc
ESP32 Micro Controller
BME280 Temp Humidity Sensor
OLED DISPLAY

## Slide 51: ESP32 Temp Sensor / OLED Wiring

## Slide 52: ESP32 / Temp Sensor / OLED Placement

## Slide 53: Sensor Wiring (Wemos D1 Mini)
All labels are as printed on ckt board, not schematic pins!
Function is in ()
External power is supplied to the D1 Mini via USB cable
ESP32 3.3 volt pin supplies power to all components
D1(SCL)
D2(SDA)
GND
3.3v
SCL
SDA
GND
Vcc
SCL
SDA
GND
Vcc
D1Mini 8266
BME280
OLED DISP

## Slide 54: D1 Mini Example – Jumper cable to wake up

## Slide 55: Botletics Shield Properties - Arduino
Botletics Shield has 2 voltage inputs
  LiPo Battery to meet surge current requirements for SIM7000A Radio
  Surge current can be up to .6A LTE-M or up to 2A NB-IoT
  5 volt line charges LiPo battery and provides logic voltage
3.7v LIPO 1200 mAh Battery 3.4-4.3v
Charger
Level Shifter
1.8v Rx, Tx, Pwr Modem
5v In
VBAT
VBAT 3.7v Radio
SIM7000A
1.8v
5v Out
Arduino
5v Rx, Tx, Pwr pulse
Botletics Shield
(3 - 4.3v)

## Slide 56: Botletics – Workaround 1
Replace the Arduino, dump the battery, and use the LTE-M band
A dedicated 3.3v .8A regulator handles SIM7000A radio
ESP32 3.3v feeds into shield 5v In to the level shifter
xxx1117 3.3v Regulator
Charger
Level Shifter
1.8v Rx, Tx, Pwr Modem
5v In
VBAT
VBAT 3.7v Radio
SIM7000A
1.8v
3.3v
ESP32
3.3v Rx, Tx, Pwr pulse
Botletics Shield
Wall Wart
(3 - 4.3v)

## Slide 57: Botletics – Workaround 2
Route The ESP32 3.3v to the battery input
Verify your ESP32 uses a LM1117 or AMS1117 or equivalent regulator
Charger
Level Shifter
1.8v Rx, Tx, Pwr Modem
5v In
VBAT
VBAT 3.7v Radio
SIM7000A
1.8v
3.3v Out
ESP32
3.3v Rx, Tx, Pwr pulse
Botletics Shield

## Slide 58: Hub Wiring (ESP32)
ESP32 3.3 volt pin supplies power to all components
Connect Botletics 5V to VBAT
Add 3 wires: Rx, Tx, Power + I2C temperature sensor option
D22(SCL)
D21(SDA)
GND
3.3v
D16(Tx2)
D17(RX2)
D18
SCL
SDA
GND
5V
VBAT
11 (RX2)
10 (TX2)
7 (Pwr)
SCL
SDA
GND
Vcc
SCL
SDA
GND
Vcc
ESP32
BME280
OLED DISP
BOTLETICS ARDUINO SHIELD
MCP9808

## Slide 59: Ambient_HUB Power Issue
Botletics Power On/Off can get out of sync with ESP32
  Pulse width determines power state; 72ms pulse ON; 1.2 sec OFF
  Condo living comes with noisy electromagnetic effects
  Occasional hangup is cured by timer to reboot Hub
D22(SCL)
D21(SDA)
GND
3.3v
D16(Tx2)
D17(RX2)
D18
SCL
SDA
GND
5V
VBAT
11 (RX2)
10 (TX2)
7 (Pwr)
SCL
SDA
GND
Vcc
SCL
SDA
GND
Vcc
ESP32
BME280
OLED DISP
BOTLETICS

## Slide 60: Hub Progression
Oct 2020 Maine
May 2021 Florida 4.5x3.5x2”
Oct 2021 Maine 4x2.7x1.5”
Breadboard
Botletics powered separately
DHT11 temp sensor
OLED display
Alert Mode
Optical sensor
Double wired
ElectroCookie PCB shield
Botletics powered separately
External BME280 temp sensor
OLED display
Alert Mode
Arduino PCB shield
Botletics powered by ESP32
Internal BME280 temp sensor
OLED display
Snooze Mode
Ventilation holes drilled in case

## Slide 61: Hub Progression - Oct 2020 Maine

## Slide 62: Hub Progression – May 2021 Florida

## Slide 63: IFTTT Event Applet Ingredients
Cells A2, B2, and C2 are updated with date time, Web event name (HB for heartbeat or AL for ALERT), and the JSON Value1 so that Home Assistant can be used to monitor those cells instead of chasing after the newest row.

## Slide 64: IFTTT Weather Applet Ingredients

## Slide 65: Ambient_AP Software Parameters
In the first section at the top of the software:
Comment one of the following lines (//) to select processor
  #define ESP32
  // #define ESP8266 (commented by default)
Choose between alert mode or Snooze mode (default)
  const int sleepSeconds = 8*60; //sleep time in seconds (default)
  // 0 if no sleep (alert mode)
  const long awakeSeconds = 2*60; //interval in seconds to stay //awake as server;
  If sleepSeconds is set to 0, awakeSeconds is ignored

## Slide 66: Ambient_AP Software Parameters
Each sensor needs unique display title and ssid; uncomment one triplet and comment the others before compiling
  //uint8_t sensorID = 1;
  //#define displayTitle " ~AMBIENT 1~"
  //const char* ssid = "AMBIENT_1";
  uint8_t sensorID = 2;
  #define displayTitle " ~AMBIENT 2~"
  const char* ssid = "AMBIENT_2";
  //uint8_t sensorID = 3;
  //#define displayTitle " ~AMBIENT 3~"
  //const char* ssid = "AMBIENT_3";

## Slide 67: Ambient_HUB Software Parameters
Enter your IFTTT key in place of ENTER_KEY
  #define IFTTT_HB_URL "http://maker.ifttt.com/trigger/HB/with/key/ENTER_KEY"
Choose between alert mode or snooze mode (default)
  const int espSleepSeconds = 48*60; //sleep time in seconds (default)
  // 0 if no sleep (alert mode)
  const long espAwakeSeconds = 12*60; // interval in seconds to stay //awake as HUB;
  If espSleepSeconds is set to 0 (alert mode), espAwakeSeconds is ignored

## Slide 68: Gotcha’s – A Consolidated List
  Voltage to the Botletics pin cannot drop below 3.0v while current could spike to 600 ma during connection and data transfer on LTE-M; 2A on NB-IoT
    Software selects LTE-M band
  LIPO batteries built for toys have different polarity than those built for electronics??; doublecheck your battery polarity if you use one
  WEMOS D1 Mini (esp8266) can have inadequate rf range, possible wifi library issues, and interfere with each other if >1?
  Verify regulators on ESP32’s! Need xx1117 or equivalent to handle LTE-M
  SIM sockets can be tinny, easily bent – Handle with care!
  Put a timer with battery backup to reset the hub periodically!

## Slide 69: Hologram: Cellular Connectivity to the Cloud
Dashboard for deployed device management and control
Data can be massaged and routed to other services
Messages can be sent to devices from the dashboard
Individual sensors can be analyzed
For example: the next slide reveals that IFTTT may be throttling by refusing data periodically
OR
It might be a software issue to test on my duplicate system

## Slide 70: Hologram Dashboard Provides Connection Details
Connection Overview
Network Connections in the Last 48 Hours
Recent Data Sessions

## Slide 71: References

## Slide 72: References
Paul McWhorter Arduino
  A series of YouTube videos which show you how to install the IDE and get started programming the Arduino microcontroller
Random Nerd Tutorials
  Step by step instructions explaining various arduino-based esp32 and esp8266 microcontrollers, projects, protocols, and much more. They include plenty of working project code

## Slide 73: References
The Guy with the Swiss Accent
Hands on Tech The Villages Florida
See H.O.T meeting 11/30/2017 and on-ramp material for detailed steps to set up IFTTT account and the Arduino IDE
Botletics Wiki, Botletics GitHub

## Slide 74: FCC Notice (47 CFR 2.803)
The following notice accompanys the Botletics shield:
“This kit is designed to allow:
(1) Product developers to evaluate electronic components, circuitry, or software associated with the kit to determine whether to incorporate such items in a finished product and…

## Slide 75: …FCC Notice (47 CFR 2.803) para 2
…(2) Software developers to write software applications for use with the end product. This kit is not a finished product and when assembled may not be resold or otherwise marketed unless all required FCC equipment authorizations are first obtained. Operation is subject to the condition that this product not cause harmful interference to licensed radio stations and that this product accept harmful interference. Unless the assembled kit is designed to operate under part 15, part 18 or part 95 of this chapter, the operator of the kit must operate under the authority of an FCC license holder or must secure an experimental authorization under part 5 of this chapter.”